## Slide 1: Building “GIANTS” Grid-edge Integration and Aggregation Network of Thermal Storage
Grid Resilience and Innovation Partnerships Program DE-FOA-0002740, Smart Grid Grants Concept Paper ID Code: TA2-380-E

## Slide 2: Building GIANTS TECHNOLOGY SUMMARY
Overview
Focus on advancing grid-interactive efficient buildings with two programs:
  Commercial & Industrial Flexible Load Management (C&I FLM)
  Residential Heat Pump Flexible Load Management (HP FLM)
Thermal energy storage uses thermal mass stored within buildings’
envelope, enabled via dynamic AC1 scheduling
BED is currently piloting these two projects with initial success with
three (3) C&I buildings and nine (9) residential homes with heat pumps
BED is an Energy Efficiency, Distribution and Generation Utility, with
wide range of expertise contributing to this project proposal.
C&I Technology
Integrate using building management system (BMS) and Dynamic Organics grid-edge controller
BACnet, MODBUS and SCADA protocols used to issue thermal schedules tailored to participating C&I customers
HP Technology
Emporia Vue submeters HP interval data (15-minute) and fossil fuel (if applicable) to enable bill credits
Sensibo Air controller allows BED to alter AC state by HP head unit.
1 Air conditioning (AC) applies to heating and cooling a space within a building or facility
Figure 1: BED’s approach to reaching the Burlington Net Zero Energy Goal by 2030 is to approach buildings using this pyramid structure. BED has expertise in energy efficiency, which translates to greater thermal capacity and flexibility
Figure 2: Sensibo Air (left) and Emporia Vue device (above)

## Slide 3: Building GIANTS IMPACT & GOALS
C&I FLM Impact
Integrate 45 C&I Buildings
Achieve 2.25 MW of dispatchable thermal storage
HP FLM IMPACT:
1,500 household in three years
1.75 MW of Flexible Thermal Storage
Enroll +600 disadvantaged community households (40%)
Combined GOALS:
Workforce Development & Collaboration across building controls
contractors, electricians, dynamic organics, and BED
Community Partnerships and greater DEIA engagement / enrollment
Integration of distribution level renewable energy resources
Accelerate transition to renewable thermal energy
Leverage FLM to defer distribution system upgrades, and benefit from wholesale electric markets, transmission and capacity savings
Figure 3: Flexible load management in the C&I sector with two buildings in Burlington shows significant potential for flexibility. These facilities include BED’s office building’s HVAC (left) and the chiller of an ice rink (right).
Figure 4: Flexible load with heat pumps tested during the current HP FLM Pilot program with nine (9) residential customers in Burlington with demand response (DR) events along with Sensibo’s App interface, though BED interfaces through Sensibo’s API for AC state adjustments.

## Slide 4: Building GIANTS PROJECT DETAILS
Phase 1: Workforce Development
Partnerships with
workforce, labor
unions, and community
organizations
Phase 2: Accelerating Deployment
Achieve 4 MW of flexible thermal load management
Focus on Justice 40 / DEIA customers
Phase 3: Marginal Cost Reduction
Efficiency through scale and process improvement
Leveraging internal expertise with energy efficiency, software programming and distribution engineering
Project Details
Title: Building Grid-edge Integration and Aggregation Network of Thermal Storage
Requested DOE Funds: $2.318 M
Estimated Project Start: 1/1/2024
Proposed Project End: 12/31/2026
BED cost share: 50%
Key Personnel
James Gibbons1 Director, Policy & Planning
Frederick Hall2 Resource Planner, MS Complex Systems
Chris Burns Director, Energy Services
Emily Stebbins-Wheelock CFO & Manager of Strategy & Innovation
Bradley Williams Senior Operation Engineer
Jennifer Green Director, Sustainability & Workforce Dev.
Ita Meno Project & Equity Analyst
Jake Yanulavich C&I Energy Services Engineer
Bob Bolin C&I Energy Services Engineer
1 Business Point of Contact
2 Technical Point of Contact and Primary Investigator